## Slide 1: AI for Energy: Data-efficient and explainable algorithms to exploit energy flexibility
Chris Develder, et al. AI4E Team, IDLab, Ghent University – imec

## Slide 2: Self-Introduction – Chris Develder[1]
Professor at Ghent University, Belgium, since Oct. 2007
    Research Interests: - AI4E Team: Artificial intelligence for energy applications:[2] data analysis & machine learning for the energy transition - T2K Team: Natural language processing (NLP):[3] information extraction (IE), conversational agents, etc. - Past: track record in dimensioning and optimizing optical networks
    Visiting researcher at UC Davis, CA, USA, Jul-Oct. 2007 (optical networks)
    Visiting researcher at Columbia Univ., NY, USA, 2013-15 (IE & information retrieval)
Industry Experience: Network planning/design tools
    Former OPNET Technologies, 2004-2005
PhD in optical networking, UGent, 1999-2003
  [1] http://users.ugent.be/~cdvelder/
  [2] https://ugentai4e.github.io/
  [3] https://ugentt2k.github.io/

## Slide 3: The AI4E team at IDLab, Ghent University
https://ugentai4e.github.io/

## Slide 4: AI for Energy: Data-efficient and explainable algorithms to exploit energy flexibility
Chris Develder, et al. AI4E Team, IDLab, Ghent University – imec

## Slide 5: Energy Transition – Supply
~ 6% share of
Wind and Solar
Increased to
~ 28% in 2020
Expected to reach
~ 45% by 2035
Source: Adequacy & flexibility study for Belgium (2024-2034), ELIA

## Slide 6: Energy Transition – Demand
~ 6% share of
EVs and Heating
Expected to reach ~ 25%
Source: Adequacy & flexibility study for Belgium (2024-2034), ELIA
HISTORICAL AND FORECASTED DEMAND IN BELGIUM

## Slide 7: SMART GRID
Distributed generation (large scale)
Green energy sources (fluctuating)````````
Distributed generation
(small scale)
Local energy storage
Demand side management
ICT infrastructure
Fault detection? Restoration? Data processing?
Privacy, security?
Pricing schemes?
. . .
EV charging
(car parks)
EV charging
(residential)
Heat pumps
New services & business models
Notes: Explain the changing power grid:
Distributed generation:
  Small scale, local (residential, companies, etc.) & Large scale (e.g. offshore wind parks)
  Problems associated with them: power quality (voltage, frequency instability…; phase balancing)
  Integration of (electric) energy storage: cost, capacity, level
Electric Vehicles => Rising Energy demand
Smart Metering (technology that enables/stimulates many other smart grid applications)
Integration of ICT and Power Grids
  Interoperability and openness of the smart grid
  Autonomous services deployed as a cloud service (privacy)
Balancing
Illustrate the scale of both networks and how the size of them will explode the following years (kickoff for next slide)
  Power: Resulting from electrification (e.g. vehicles)
  ICT: Everything connected everywhere
  Combination of both (new/existing electrical components that will become connected and intelligent)

## Slide 8: Outline
PART I: Physics-informed reinforcement learning
Challenge: Learn suitable control policy from limited data
Solution: Infuse a priori physics knowledge into neural network model
PART II: Interpretable decision trees
Challenge: Policies from RL are black-box and non-trivial to deploy
Solution: Distill a learned policy into decision tree
PART III: Real-world testbed environment
HomeLabGym: Standardized interface to experiment with real house
HomeLabGym
Notes: Ne

## Slide 9: PART I: Physics-informed reinforcement learning for residential heat pump control
G. Gokhale, B. Claessens, and C. Develder, ”PhysQ: A physics-informed reinforcement learning framework for building controls”, Arxiv preprint, 21 Nov. 2022, arXiv:2211.11830v1
Thanks
Gargya!
G. Gokhale, B. Claessens, and C. Develder, ”Physics-informed neural networks for control-oriented thermal modeling of buildings”, Appl. Energy, Vol. 314, 15 May 2022, pp. 1-10. doi:10.1016/j.apenergy.2022.118852

## Slide 10: Residential heat pump control: Problem statement & proposed solution
Objective:
  Minimize cost of energy consumed by a household while maintaining thermal comfort
Controller should:
  Use data efficiently
  Scale across different households
  Yield high-quality control policies
Proposed Solution:
  Off-policy reinforcement learning with physics informed neural networks

## Slide 11: Reinforcement Learning: Agent acts in an environment
At each timestep t the agent
  Gets state observation st
  Gets scalar reward rt (depending on current state and thus previous action(s))
  Decides to take action at
The environment
  Receives action at
  Emits state st +1 (which will depend on action)
  Emits scalar reward rt + 1
RL idea: learn a policy that maps state st to action at , such that long-term reward ∑rt is maximized
State
Reward
Action
st
rt
at

## Slide 12: Reinforcement Learning: Agent acts in an environment
At each timestep t the agent
  Gets state observation st
  Gets scalar reward rt (depending on current state and thus previous action(s))
  Decides to take action at
The environment
  Receives action at
  Emits state st +1 (which will depend on action)
  Emits scalar reward rt + 1
RL idea: learn a policy that maps state st to action at , such that long-term reward ∑rt is maximized
State
Cost
Action
st
rt
at
HEM
controller
€

## Slide 13: Reinforcement Learning: Heat pump control
HEM
controller
- outdoor T
- indoor T
- price
- time
state
action
heat pump power

## Slide 14: PhysQ: A physics-informed reinforcement learning framework
PhysQ:
  Physics informed RL framework
  Leverages prior physics to learn physically relevant latent representations
  Learns a control policy using this latent representation
Two-step Algorithm:
  Step 1: Learn physically relevant representation (bulk temperature Tm), from predicting state transitions
Idea:
Include bulk temperature as part of representation, and
Force it to adhere to simplified physical model
```

## Slide 15: PhysQ: A physics-informed reinforcement learning framework
PhysQ:
  Physics informed RL framework
  Leverages prior physics to learn physically relevant latent representations
  Learns a control policy using this latent representation
Two-step Algorithm:
  Step 1: Learn physically relevant representation (bulk temperature Tm), from predicting state transitions
  Step 2: Learn a low-dimensional Q-function based on this representation, to perform the actual control

## Slide 16: Simulation results
Results for BELPEX prices using a building simulator
Comparison over different training data sizes and agent types
On
Lower overall cost,
especially for low volumes of training data
Black box models
Off
Heating at (relatively) low price points

## Slide 17: Simulation results
Results for BELPEX prices using a building simulator
Comparison over different training data sizes and agent types
On
Lower overall cost,
especially for low volumes of training data
Black box models
Off
Heating at (relatively) low price points

## Slide 18: PART II: Interpretable decision trees distilled from black-box RL policies
G. Gokhale, S.S. Karimi Madahi, B. Claessens and C. Develder, "Distill2Explain: Differentiable decision trees for explainable reinforcement learning in energy application controllers", in Proc. 15th ACM Int. Conf. Future Energy Sys. (e-Energy 2024), Singapore, 4-7 Jun. 2024, pp. 1-8. doi:10.1145/3632775.3661937
Thanks
Gargya!

## Slide 19: Black-box Reinforcement Learning
HEM
controller
- outdoor T
- indoor T
- time
- load
- PV power
- . . .
state
action
- heat pump power
- battery power
- . . .
Black-box model: cannot explain why a given action is chosen . . .

## Slide 20: Black-box Reinforcement Learning
HEM
controller
- outdoor T
- indoor T
- time
- load
- PV power
- . . .
state
action
- heat pump power
- battery power
- . . .
Idea: replace neural networks by something more explainable!

## Slide 21: Enhancing explainability: Differentiable Decision Trees
PV power > 0.47
Load > 0.68
PV power > 0.41
[0.385, 0.413, 0.076, 0.069, 0.057]
[0.060, 0.082, 0.304, 0.344, 0.210]
[0.077, 0.081, 0.418, 0.071, 0.353]
[0.378, 0.384, 0.087, 0.097, 0.053]
Discharge at 50% power
Charge at 50% power
Discharge at 50% power
Remain idle
yes
no
yes
no
yes
no
Load > 0.68
PV power > 0.47
[0.060, 0.082, 0.304, 0.344, 0.210]
“If it is sunny and household load is low, then charge battery”

## Slide 22: Distill2Explain: Learns the tree from trained RL policy
Step 2: distill a decision tree “student” model
State
Cost
Action
€
Step 1: train an RL “teacher” model

## Slide 23: Distill2Explain: Learns the tree from trained RL policy
Step 2: distill a decision tree “student” model
State
Cost
Action
€
Step 1: train an RL “teacher” model
How? E.g., see [1] on how to disill soft decision trees.
We learn deterministic trees
[1] Y. Coppens, K. Efthymiadis, T. Lenaerts, A. Nowé, T. Miller, R. Weber, and D. Magazzeni, “Distilling deep reinforcement learning policies in soft decision trees”, In Proc. IJCAI 2019 Workshop on Explainable AI, pp. 1–6.

## Slide 24: Sample result: Home battery control under time-varying pricing
Household with rooftop PV and battery
Day-ahead pricing (qh based) and capacity tariff (= based on max. peak load)
Cost (€)
5
10
15
20
Baseline RBC
DQN
DDT
depth 2
DDT
depth 3
DQN
DDT
depth 2
DDT
depth 3
Comparable cost . . .
DQN
DDT
depth 2
DDT
depth 3
with simpler policies

## Slide 25: PART III: A real-world testbed environment: HomeLabGym
Thanks
Toon!
T. Van Puyvelde, M.-S. Verwee, G. Gokhale, M. Zareh Eshdoust and C. Develder, "HomeLabGym: A real-world testbed for home energy management systems", in Proc. 15th ACM Int. Conf. Future Energy Sys. (e-Energy 2024), Singapore, 4-7 Jun. 2024, pp. 1-2. doi:10.1145/3632775.3661974

## Slide 26
HomeLab
Research infrastructure to validate and optimize IoT & AI innovations in real environment
>300 sensors (temperature, energy, light, occupancy, …)
HVAC, ESS, PV
Controllable blinds and windows
. . .
Notes: HomeLab is an initiative of imec and Ghent University. It is both a home and a lab as it is a two-story house in which people can live temporarily to test and co-create IoT prototypes or products. With technical corridors in every room and an open home automation system, it offers tremendous flexibility to develop and install early prototypes of smart products and test their interoperability with other systems.
It focuses on testing and co-developing smart home innovations in a variety of application domains – from home automation and (health)care to entertainment, energy and security. It aims at serving the needs of SMEs as well as large businesses, researchers, non-profit organizations, etc.
It is located on the Technology Campus Ghent in Belgium
www.imec-int.com/homelab

## Slide 27
Home battery
Energy consumption monitoring per wall socket and building system (> 150 measurement points)
5kWp solar panels
Controllable heat pump + low temperature radiators + controllable valves
2 ventilation systems with controllable valves to living room and meeting rooms
Controllable blinds & windows
Energy infrastructure
Collab w/
PhD funded by
Notes: The cellar holds the HVAC (heating, ventilation, and air conditioning) equipment (2 ventilation systems with top cooling + heat pump), and the extended electrical cabinets . On the roof 5kWp solar panels are installed
HomeLab features an open home automation system (Velbus) able to control and monitor all functional elements (screens, switches, doors, windows, etc.) in the house.
Multiple vendor systems can be installed simultaneously in order to validate or benchmark building automation components or services.

## Slide 28: HomeLabGym
Controller
action
next state,
reward
?
Focus of our research: controllers, based on reinforcement learning, to exploit energy flexibility

## Slide 29: HomeLabGym
Wishlist:
Standardized approach
Plug-and-play
Extensible solution
Broad range of communication protocols
. . .
Controller
action
next state,
reward

## Slide 30: HomeLabGym
HomeLabGym
PV
Battery
Heat Pump
Modbus, API, TCP/IP
Docker, Grafana
. . .
Standardized interface, used for many RL benchmarks (cf. OpenAI gym environments)
Controller
action
next state,
reward

## Slide 31: HomeLabGym
Controller
action
next state,
reward
HomeLabGym
PV
Battery
Heat Pump
Modbus, API, TCP/IP
Docker, Grafana
. . .
HomeSimGym
(Matlab engine)

## Slide 32: HomeLabGym
Controller
action
next state,
reward
HomeLabGym
PV
Battery
Heat Pump
Modbus, API, TCP/IP
Docker, Grafana
. . .
HomeSimGym
(Matlab engine)

## Slide 33: Example use case for HomeLabGym: Validation of RL for energy arbitrage
S.S. Karimi Madahi, G. Gokhale, M.-S. Verwee, B. Claessens and C. Develder, "Control policy correction framework for reinforcement learning-based energy arbitrage strategies", in Proc. 15th ACM Int. Conf. Future Energy Sys. (e-Energy 2024), Singapore, 4-7 Jun. 2024, pp. 1-9.. doi:10.1145/3632775.3661948
Thanks
Soroush!
Case study:
  Home battery
  Time-varying prices (qh-based)
  Distributional DQN strategy accounting
Validation of simulation
  Real-world battery
  Using HomeLabGym
Results
  Latency in communication (~10s)
  Battery efficiency affected by temperature
  Effect on daily revenue: real profit €5.6 vs. simulated €6

## Slide 34: Thank you! Any questions?
It’s not easy
being green …
chris.develder@ugent.be
http://users.ugent.be/~cdvelder https://ugentai4e.github.io

## Slide 35: The AI4E team at IDLab, Ghent University
https://ugentai4e.github.io/

## Slide 36: AI4E: DATA-DRIVEN SOLUTIONS
Data-efficient
Control
Scalable Flexibility Exploitation
Predictive Support Tools

## Slide 37: RESEARCH TRACKS
Data-driven decision making for . . .
Home Energy Management (HEM)
  Value stacking (capacity tariff / dynamic pricing / ...)
  Heterogeneous households (Heat pump / EV / Home battery / Thermal Storage)
Real/short-time (24h down to 1s) flexibility optimization
  Multi-market day-ahead and real-time trading in energy and flexibility markets (EU/UK)
  Multi-asset flexibility coordination, focusing on residential flexibility
Support tools for power system operators
  Decision support for consumer-centric market vision (Imbalance forecasting; RTP price calculations; digital twins …)
  State estimation and forecasting (DSO/TSO)

## Slide 38: TECHNOLOGY
Creating scalable / practical / intuitive / performant AI that is . . .
fit-for-purpose (provide a solution, not a method)
a holistic solution, not just an optimizer (incl. technical/regulatory/legal/... constraints)
Focusing on
Neural network architectures, e.g.:
  Physics-informed neural networks and transfer learning: obtain practical and intuitive (explainable) solutions
  Graph Neural Networks (natural fit with power systems): trading / grid solutions / agent interactions
  Architectures that can handle long time series (e.g., transformers)
Data-driven decision making
  Blending rule-based (apprentice learning) / model-based (MPC) / model-free (Reinforcement Learning)
  Transfer learning and multi-agent decision making