## Slide 1: AI for Energy: Data-efficient and explainable algorithms to exploit energy flexibility
Chris Develder, et al. AI4E Team, IDLab, Ghent University – imec

## Slide 2: Energy Transition
RES share in EU electricity supply: ~45% by 2035
Source: Adequacy & flexibility study for Belgium (2024-2034), ELIA
e-Mobility + Heat pumps
in BE electricity demand: ~25% by 2035
Source: Adequacy & flexibility study for Belgium (2024-2034), ELIA

## Slide 3: AI4E: VISION
Research, develop and incubate data-driven (decision making) technology supporting decarbonization of our society through co-creation with industry & research partners

## Slide 4: AI4E: FIT-FOR-PURPOSE & HOLISTIC SOLUTIONS
Data-efficient
Control
Scalable Flexibility Exploitation
Predictive Support Tools
Neural Networks
Reinforcement Learning
Graph Neural Networks
. . .

## Slide 5: AI4E Research Tracks
Data-driven decision making for . . .
Home Energy Management (HEM)
  Value stacking (capacity tariff / dynamic pricing / . . .)
  Heterogeneous households (Heat pump / EV / Home battery / Thermal Storage)
Real/short-time (24h down to 1s) flexibility optimization
  Multi-market day-ahead and real-time trading in energy and flexibility markets (EU/UK)
  Multi-asset flexibility coordination, focusing on residential flexibility
Support tools for power system operators
  Decision support for consumer-centric market vision (Imbalance forecasting; RTP price calculations; digital twins . . .)
  State estimation and forecasting (DSO/TSO)

## Slide 6: Data-efficient learning to control: Physics-informed RL for residential heat pumps
G. Gokhale, B. Claessens, and C. Develder, ”PhysQ: A physics-informed reinforcement learning framework for building controls”, Arxiv preprint, 21 Nov. 2022, arXiv:2211.11830v1
Thanks
Gargya!
G. Gokhale, B. Claessens, and C. Develder, ”Physics-informed neural networks for control-oriented thermal modeling of buildings”, Appl. Energy, Vol. 314, 15 May 2022, pp. 1-10. doi:10.1016/j.apenergy.2022.118852
Home Energy Management

## Slide 7: Reinforcement Learning: Heat pump control
HEM
controller
- outdoor T
- indoor T
- price
- time
state
action
heat pump power
Challenge: Learn good policy from little data!

## Slide 8: Reinforcement Learning: Agent acts in an environment
At each timestep t the agent
  Gets state observation st
  Gets scalar reward rt (depending on current state and thus previous action(s))
  Decides to take action at
The environment
  Receives action at
  Emits state st +1 (which will depend on action)
  Emits scalar reward rt + 1
RL idea: learn a policy that maps state st to action at , such that long-term reward ∑rt is maximized
State
Reward
Action
st
rt
at

## Slide 9: Reinforcement Learning: Agent acts in an environment
At each timestep t the agent
  Gets state observation st
  Gets scalar reward rt (depending on current state and thus previous action(s))
  Decides to take action at
The environment
  Receives action at
  Emits state st +1 (which will depend on action)
  Emits scalar reward rt + 1
RL idea: learn a policy that maps state st to action at , such that long-term reward ∑rt is maximized
State
Cost
Action
st
rt
at
HEM
controller
€

## Slide 10: PhysQ: A physics-informed reinforcement learning framework
PhysQ:
  Physics informed RL framework
  Leverages prior physics to learn physically relevant latent representations
  Learns a control policy using this latent representation
Two-step Algorithm:
  Step 1: Learn physically relevant representation (bulk temperature Tm), from predicting state transitions
  Step 2: Learn a low-dimensional Q-function based on this representation, to perform the actual control
Idea:
Add physical quantity (following laws of physics) to representation
Here: building mass temperature; learn it from indoor temp. prediction
state

## Slide 11: PhysQ: A physics-informed reinforcement learning framework
PhysQ:
  Physics informed RL framework
  Leverages prior physics to learn physically relevant latent representations
  Learns a control policy using this latent representation
Two-step Algorithm:
  Step 1: Learn physically relevant representation (bulk temperature Tm), from predicting state transitions
  Step 2: Learn a low-dimensional Q-function based on this representation, to perform the actual control
Idea:
Use that representation (incl. physics) to learn control actions
state

## Slide 12: Simulation results
Results for BELPEX prices using a building simulator
Comparison over different training data sizes and agent types
On
Lower overall cost,
especially for low volumes of training data
Black box models
Off
Heating at (relatively) low price points

## Slide 13: Simulation results
Results for BELPEX prices using a building simulator
Comparison over different training data sizes and agent types
On
Black box models
Off
Heating at (relatively) low price points
Lower overall cost, especially for low training data volume

## Slide 14: Interpretable decision trees distilled from black-box RL policies
Home Energy Management
Thanks
Gargya & Toon!
T. Van Puyvelde, M. Zareh and C. Develder, "Interpretable reinforcement learning for heat pump control through asymmetric differentiable decision trees", in Proc. AI-Driven Energy Effic. Dyn. Syst. (AI-DEEDS 2025) at ACM e-Energy 2025, Rotterdam, The Netherlands, 17 Jun. 2025, pp. 968-972. doi:10.1145/3679240.3734671
G. Gokhale, S.S. Karimi Madahi, B. Claessens and C. Develder, "Distill2Explain: Differentiable decision trees for explainable reinforcement learning in energy application controllers", in Proc. 15th ACM Int. Conf. Future Energy Sys. (e-Energy 2024), Singapore, 4-7 Jun. 2024, pp. 1-8. doi:10.1145/3632775.3661937

## Slide 15: Black-box Reinforcement Learning
HEM
controller
- outdoor T
- indoor T
- time
- load
- PV power
- . . .
state
action
- heat pump power
- battery power
- . . .
Challenge: Find a good policy that is explainable

## Slide 16: Black-box Reinforcement Learning
HEM
controller
- outdoor T
- indoor T
- time
- load
- PV power
- . . .
state
action
- heat pump power
- battery power
- . . .
Challenge: Find a good policy that is explainable
Idea: replace neural networks by decision trees derived from it!

## Slide 17: Enhancing explainability: Differentiable Decision Trees
PV power > 0.47
Load > 0.68
PV power > 0.41
[0.385, 0.413, 0.076, 0.069, 0.057]
[0.060, 0.082, 0.304, 0.344, 0.210]
[0.077, 0.081, 0.418, 0.071, 0.353]
[0.378, 0.384, 0.087, 0.097, 0.053]
Discharge at 50% power
Charge at 50% power
Discharge at 50% power
Remain idle
yes
no
yes
no
yes
no
Load > 0.68
PV power > 0.47
[0.060, 0.082, 0.304, 0.344, 0.210]
“If it is sunny and household load is low, then charge battery”
discharge
at 100% power
discharge
at 50% power
idle
charge
at 50% power
charge
at 100% power
[
]
,
,
,
,
Action probabilities:

## Slide 18: Sample result: Home battery control under time-varying pricing
Household with rooftop PV and battery
Day-ahead pricing (qh based) and capacity tariff (= based on max. peak load)
Cost (€)
5
10
15
20
Baseline RBC
DQN
DDT
depth 2
DDT
depth 3
DQN
DDT
depth 2
DDT
depth 3
Comparable cost . . .
DQN
DDT
depth 2
DDT
depth 3
Low Load
Med. Load
High Load
Normalized Cost
with simpler policies
Battery state-of-charge

## Slide 19: Sample result: Heat-pump control
Same idea applied to space heating with a heat pump (= minimization of cost while maintaining comfort)
Extended methodology to allow asymmetric trees (= branches can have different depths)
Performance approaches teacher model (DQN) for larger decision trees
Assymmetric trees =
Better performance for same size!

## Slide 20: Scalable Attention-based RL for Multi-asset Control
Flexibiity Optimization
Thanks
Soroush & Giuseppe!
G. Gabriele, F. Pavirani, S.S.K. Madahi, and C. Develder, "Forecasting what matters: Decision‑focused RL for controlled EV charging with unknown departure times", in Proc. 17th ACM Int. Conf. Future Energy Sys. (e-Energy 2026), Banff, Canada, 23-25 Jun. 2026, pp. 235-239. doi:10.1145/3744255.3811736
S.S. Karimi Madahi, G. Gabriele, B. Claessens and C. Develder, "Scalable attention-based reinforcement learning method for multi-asset control", in Proc. Workshop Comput. Optim. Buildings (CO-BUILD) at ICML 2025, Vancouver, Canada, 18 Jul. 2025, pp. 1-8.. https://openreview.net/attachment?id=3h0v1Ht73L&name=pdf

## Slide 21: Controlling EV charging
Why?
  Limit peak load
  Limit charging costs
  Balancing
  . . .
How?
  Identify EV requirements (timing + energy)
  Automatic control algorithm
t2
t3
AI for EV charging =
(1) KNOWING and (2) CONTROLLING EV sessions

## Slide 22: Step 1: Charging session characterization
Daytime charging
(9.4%)
Anytime charging, short sojourn (61.5%)
Nighttime charging (29.1%)
C. Develder, N. Sadeghianpourhamami, M. Strobbe and N. Refa, "Quantifying flexibility in EV charging as DR potential: Analysis of two real-world data sets", in Proc. 7th IEEE Int. Conf. Smart Grid Communications (SmartGridComm 2016), Sydney, Australia, 6-9 Nov. 2016, pp. 600-605.
N. Sadeghianpourhamami, N. Refa, M. Strobbe and C. Develder, “Quantitative analysis of electric vehicle flexibility: A data-driven approach”, Int. J. Electr. Power Energy Syst., Vol. 95, Feb. 2018, pp. 451-462.
M. Lahariya, D.F. Benoit and C. Develder, “Synthetic data generator for electric vehicle charging sessions: Modeling and evaluation using real-world data", Energies, Vol. 13, Issue 16, Paper no. 4211, 2020.
Thanks
Nasrin & Manu!

## Slide 23: Step 2: Scalable RL controller
At each timestep t the agent
  Gets state observation
  Decides to take action
The environment
  Receives action at
  Transitions to state st +1
  Returns scalar reward
State
Reward
DistSAC
st
rt
at
Action
Goal: Minimize peak load + Charge EVs on time

## Slide 24: Step 2: Attention-based state representations for scalable RL
Idea:
Construct state representation combining own asset + relative to other assets + global state
Use state representation as input representation in conventional RL (e.g., to map to Q-value, action, …)
N

## Slide 25: Simulation Results
*: 27% is the average over full test set
Attention-based RL
Flattens load (peak reduced by 27%)*
Performs close to optimization based on perfect foresight
Significant peak reduction compared to uncontrolled charging
BAU
Notes: Ne

## Slide 26: Simulation Results
Attention-based RL
Flattens load (peak reduced by 27%)*
Performs close to optimization based on perfect foresight
*: 27% is the average over full test set
Peak reduction of our RL solution is very close to optimal control (w/ perfect foresight)
BAU
Notes: Ne

## Slide 27: Imbalance price prediction with Monte Carlo Tree Search (MCTS)
Support Tools for DSO & TSO
Thanks
Fabio & Jonas!
J. Van Gompel, B. Claessens and C. Develder, "Probabilistic forecasting of power system imbalance using neural network-based ensembles", Appl. Energy, Vol. 401, Part B, No. 126714, Dec. 2025. doi:10.1016/j.apenergy.22025.126714
F. Pavirani, J. Van Gompel, S.S. Karimi Madahi, B. Claessens and C. Develder, "Predicting and publishing accurate imbalance prices using Monte Carlo Tree Search", Appl. Energy, Vol. 392, No. 125944, 15 Aug. 2025. doi:10.1016/j.apenergy.2025.125944

## Slide 28: Maintaining System Balance
Generation: Renewable sources Load: Increased electrification
Mismatch needs to be solved
  Compensation from aFRR, mFRR
  Reaction of BRPs themselves . . . where imbalance prices for BRP depend on SI
Source: https://www.elia.be/en/grid-data/balancing/imbalance-prices-15-min (Fri, April 2024, 15:00)
But … price predictions are published within the quarter! -> influences behavior of BRPs!

## Slide 29: Imbalance Price Publication
But … price predictions are published within the quarter! -> influences behavior of BRPs!
BRPs
Grid
TSO
Measured system imbalance (15’)
Publish imbalance price forecast (1’)
BRPs react to published prices

## Slide 30: MCTS Based Imbalance Price Forecasting
Net Reserve Volume (NRV) Forecaster
BRP Response
Model
MCTS = Monte Carlo Tree Search
Roll out possible scenarios, based on system model
Learn to decide best “action”
timesteps
System state
Price prediction
J. Van Gompel, B. Claessens and C. Develder, "Probabilistic forecasting of power system imbalance using neural network-based ensembles", Appl. Energy, Vol. 401, Part B, No. 126714, Dec. 2025. doi:10.1016/j.apenergy.2025.126714
S.S. Karimi Madahi, B. Claessens and C. Develder, "Distributional reinforcement learning-based energy arbitrage strategies in imbalance settlement mechanism", J. Energy Storage, Vol. 104, Part A, Dec. 2024, pp. 114377. doi:10.1016/j.est.2024.114377
Notes: System imbalance = - NRV + BRP response
Battery capacity for BRP: small (60MW, 150MWh) – medium (125MW, 310MWh) – large (250MW, 620MWh)
NRV prediction: w/o inputs correlated to BRP response; i.e., only
Time features,
SI and NRV history,
Net cross-border nominations,
PV and Wind generation forecasts, and
Load forecasts.

## Slide 31: Results: Price prediction within the quarter
Lower prediction error & lower uncertainty on estimates!
Error approaches zero towards end of quarter
Caveat: sample results for perfect NRV and BRP response models
!
Notes: Baseline = Elia’s current price formula
Battery capacity for BRP:
small (60MW, 150MWh)
medium (125MW, 310MWh)  this figure!
large (250MW, 620MWh)

## Slide 32: Results: Overall error distributions
Distributions of errors are more narrowly centered around zero!
Notes: Battery capacity for BRP:
small (60MW, 150MWh)
medium (125MW, 310MWh)
large (250MW, 620MWh)

## Slide 33: A real-world testbed environment: HomeLabGym
Home Energy Management
Thanks
Toon!
T. Van Puyvelde, M.-S. Verwee, G. Gokhale, M. Zareh Eshdoust and C. Develder, "HomeLabGym: A real-world testbed for home energy management systems", in Proc. 15th ACM Int. Conf. Future Energy Sys. (e-Energy 2024), Singapore, 4-7 Jun. 2024, pp. 1-2. doi:10.1145/3632775.3661974

## Slide 34
HomeLab
Research infrastructure to validate and optimize IoT & AI innovations in real environment
>300 sensors (temperature, energy, light, occupancy, …)
HVAC, ESS, PV
Controllable blinds and windows
. . .
Notes: HomeLab is an initiative of imec and Ghent University. It is both a home and a lab as it is a two-story house in which people can live temporarily to test and co-create IoT prototypes or products. With technical corridors in every room and an open home automation system, it offers tremendous flexibility to develop and install early prototypes of smart products and test their interoperability with other systems.
It focuses on testing and co-developing smart home innovations in a variety of application domains – from home automation and (health)care to entertainment, energy and security. It aims at serving the needs of SMEs as well as large businesses, researchers, non-profit organizations, etc.
It is located on the Technology Campus Ghent in Belgium
www.imec-int.com/homelab

## Slide 35
Home battery
Energy consumption monitoring per wall socket and building system (> 150 measurement points)
5kWp solar panels
Controllable heat pump + low temperature radiators + controllable valves
2 ventilation systems with controllable valves to living room and meeting rooms
Controllable blinds & windows
Energy infrastructure
Collab w/
PhD funded by
Notes: The cellar holds the HVAC (heating, ventilation, and air conditioning) equipment (2 ventilation systems with top cooling + heat pump), and the extended electrical cabinets . On the roof 5kWp solar panels are installed
HomeLab features an open home automation system (Velbus) able to control and monitor all functional elements (screens, switches, doors, windows, etc.) in the house.
Multiple vendor systems can be installed simultaneously in order to validate or benchmark building automation components or services.

## Slide 36: HomeLabGym
Controller
action
next state,
reward
?
Focus of our research: controllers, based on reinforcement learning, to exploit energy flexibility

## Slide 37: HomeLabGym
Wishlist:
Standardized approach
Plug-and-play
Extensible solution
Broad range of communication protocols
. . .
Controller
action
next state,
reward

## Slide 38: HomeLabGym
HomeLabGym
PV
Battery
Heat Pump
Modbus, API, TCP/IP
Docker, Grafana
. . .
Standardized interface, used for many RL benchmarks (cf. OpenAI gym environments)
Controller
action
next state,
reward

## Slide 39: HomeLabGym
Controller
action
next state,
reward
HomeLabGym
PV
Battery
Heat Pump
Modbus, API, TCP/IP
Docker, Grafana
. . .
HomeSimGym
(Matlab engine)

## Slide 40: HomeLabGym
Controller
action
next state,
reward
HomeLabGym
PV
Battery
Heat Pump
Modbus, API, TCP/IP
Docker, Grafana
. . .
HomeSimGym
(Matlab engine)

## Slide 41: Example use case for HomeLabGym: Validation of RL for energy arbitrage
S.S. Karimi Madahi, G. Gokhale, M.-S. Verwee, B. Claessens and C. Develder, "Control policy correction framework for reinforcement learning-based energy arbitrage strategies", in Proc. 15th ACM Int. Conf. Future Energy Sys. (e-Energy 2024), Singapore, 4-7 Jun. 2024, pp. 1-9.. doi:10.1145/3632775.3661948
Thanks
Soroush!
Case study:
  Home battery
  Time-varying prices (qh-based)
  Distributional DQN strategy accounting
Validation of simulation
  Real-world battery
  Using HomeLabGym
Results
  Latency in communication (up to ~10s)
  Battery efficiency affected by temperature
  Effect on daily revenue: real profit €5.6 vs. simulated €6

## Slide 42: Thank you! Any questions?
It’s not easy
being green …
chris.develder@ugent.be
http://users.ugent.be/~cdvelder https://ugentai4e.github.io

## Slide 43: The AI4E team at IDLab, Ghent University – imec
https://ugentai4e.github.io/

## Slide 44: Simulation Setup
Datasets
Historical real-world dataset of 20 EVs
  Belgian residential charging sessions
  Data split: 40d train / 5d eval / 5d test
Scaled dataset of 100 EVs
  Fit Gaussian mixture model on historical dataset
  Data split: 30d train / 7d eval / 7d test
Benchmark controllers
Business-as-usual (BAU): Start charging upon arrival
Optimal: MPC optimization with perfect foresight over full day
Departures
Arrivals
Notes: Ne

## Slide 45: MCTS based imbalance price forecasting
Cluster of RL Controller
Agents
Ensemble
Neural Network
Forecaster
Training
Data
Training
Data